## Slide 1
Week 1_ Day 3
Mentor Review
Mentor Name: Vamsikrishna
Student Name: Ettigowni Siri
OCC VIDEO MESSAGE DECODING

## Slide 2
WEEK 1_DAY 3 - MENTOR REVIEW 1
Research Framing
Refined Research Question:
Given an OCC video containing an OOK-encoded transmission, can a software-only pipeline reliably recover the transmitted binary sequence and decoded message, and how do ROI choice, smoothing, threshold, and symbol-timing decisions affect decoding accuracy?
OCC Video Message Decoding
Problem Context
Optical Camera Communication (OCC) uses a light source to transmit information through variations in light intensity.
In this project, the transmission uses On-Off Keying (OOK), where different light states represent binary information.
A camera records the transmitted signal as a video.
The objective is to recover the binary information from the recorded video using a software-only approach.
Key Factors Being Investigated
Region of Interest (ROI) selection
Light-intensity extraction from video frames
Signal smoothing and noise reduction
Threshold selection
Symbol timing and synchronization
Video quality and camera-related distortions
Expected Output
Raw OCC Video → Binary Sequence → Decoded Message
Scope: Software-only implementation, with no hardware or field deployment in the current phase.

## Slide 3
WEEK 1_DAY 3 - MENTOR REVIEW 1
Completed Work & Blockers
Completed Work — Days 1 & 2
Day 1: Problem Understanding
Studied the OCC video decoding problem.
Defined the input, processing stages and expected output.
Developed an 8-stage decoding pipeline.
Day 2: Literature Review
Reviewed 9 research papers related to OCC and signal decoding.
Compared the approaches, evaluation metrics, reported results and limitations.
Shortlisted possible approaches:
  Threshold-based baseline
  Signal-processing approach
  Multi-feature refinement
  ML-assisted classifier
Key Risks Identified
Synchronization and clock mismatch
Ambient light flickering
Rolling-shutter distortion
Limited availability of ground-truth data
Current Blockers
Exact message framing such as preamble/checksum is not confirmed.
It is unclear whether ground-truth bit sequences are available for every video.
Camera settings and recording consistency across videos need confirmation.
Need guidance on whether BER or exact-message correctness should be the primary evaluation criterion.

## Slide 4
WEEK 1_DAY 3 - MENTOR REVIEW 1
Next 3-Day Plan & Mentor Decisions
Plan — Days 4–6
DAY 4 — Dataset Readiness
Finalize dataset structure.
Verify raw videos and available ground-truth labels.
Identify missing data and possible class imbalance.
Check for potential data leakage between train/validation/test sets.
DAY 5 — Methodology & Experiments
Finalize the video-to-message pipeline.
Define the baseline decoding method.
Prepare experiments for:
  ROI selection
  Smoothing
  Thresholding
  Symbol synchronization
Set up experiment logging and repository structure.
DAY 6 — Finalization
Consolidate literature findings.
Finalize methodology and experimental plan.
Prepare the data-readiness and methodology package for Mentor Review 2.
Mentor Guidance Required
What message framing should we assume?
Is ground-truth data available for all videos?
Should evaluation prioritize BER, exact-message accuracy, or both?
What BER/error threshold should be considered acceptable?
Can we assume consistent camera settings across the dataset?
Notes: Mentor Review 1 notes: record the mentor's confirmed decisions on target definition, dataset structure, evaluation metrics, and scope here immediately after the review, then update the research-framing note (Day 3 doc) with any revised assumptions.