## Slide 1
Week 2_ Day 9
Mentor Review
Mentor Name: Vamsikrishna
Student Name: Ettigowni Siri
OCC VIDEO MESSAGE DECODING

## Slide 2
DAY 9
  ROI Selection
  ROI is selected using area-filtered connected-component detection rather than simply choosing the brightest pixel.
  Candidate bright regions are filtered based on their area to eliminate non-transmitter artifacts.
  The detected number of candidate regions is cross-checked with the expected LED count: 1, 2, 3, or 4 LEDs.
  Day 7–8 measurements show very low ROI movement for the tested videos.
  Therefore, a fixed ROI is selected for each video, avoiding unnecessary frame-by-frame re-detection.
  Dead-time regions at the beginning and end of the video are removed before ROI-based signal processing.
  Signal Extraction Strategy
  Fixed ROI → Extract ROI pixels from each frame → Calculate representative intensity → Generate temporal intensity signal
  The resulting intensity-vs-frame signal will be used for preprocessing, synchronization and message decoding.
Candidate ROI and Signal-Extraction Strategy
Video | ROI | Size | Motion
1 LED | (287,110)–(407,229) | 120 × 119 | 0.31 px
2 LEDs | (311,15)–(499,114) | 188 × 99 | 0.33 px
3 LEDs | (403,33)–(607,99) | 204 × 66 | 2.08 px
4 LEDs | (272,78)–(474,244) | 202 × 166 | 4.01 px

## Slide 3
2
Proposed Synchronization Approach
Camera frame rate = 260 fps
Transmission rate = 92 bps
Therefore:
260 / 92 = 2.826 frames per bit
  Since the ratio is non-integer, fixed-frame slicing can gradually shift the assumed symbol boundaries.
  This can cause timing drift and incorrect bit decoding over the message.
  Therefore, symbol boundaries will be recovered from actual ROI-intensity transitions rather than assuming a fixed 2.826-frame/bit relationship.
  This approach follows the synchronization issue identified in the reviewed OCC literature.
Preprocessing Freeze
The preprocessing sequence will be:
Dead-time trimming → ROI intensity extraction → Denoising / smoothing → Normalization → Transition detection
  Dead-time lead/trail regions are removed first.
  Intensity fluctuations are reduced through smoothing/denoising.
  Signal normalization reduces variations between recordings.
  Transitions in the processed signal are then used for synchronization.
Evaluation
  Decoded-message correctness: whether the complete message is correctly recovered.
  BER: calculated when ground-truth bit labels are available.
  Synchronization robustness: ability to maintain correct symbol boundaries.
  Execution time: processing time required per video.
Synchronization, Evaluation & Preprocessing Freeze

## Slide 4
ROI
  Fixed ROI per video
  Area-filtered connected-component detection
  Candidate count checked against expected LED count
Preprocessing
  Dead-time trimming
  Intensity extraction
  Denoising / smoothing
  Normalization
Synchronization
  Transition-based symbol synchronization
  No fixed-frame slicing based only on the nominal 2.826 frames/bit ratio
Evaluation
  Exact decoded-message correctness
  BER where ground truth is available
  Synchronization robustness
  Execution time
Current Open Issues
Ground Truth
No ground-truth labels file was supplied during Day 7.
BER evaluation therefore requires confirmation of whether another ground-truth source exists.
Dataset Size
Currently, there is 1 video per LED-count condition.
This is sufficient for initial pipeline testing, but not enough to make a reliable accuracy-vs-LED-count trend claim.
Approval Required
1. Approve the fixed, area-filtered ROI strategy.
2. Approve transition-based symbol synchronization.
3. Confirm whether BER evaluation is required or exact-match evaluation can be used when labels are unavailable.
4. Confirm whether the current number of videos is sufficient or additional recordings should be requested.
5. Approve freezing the above preprocessing and evaluation strategy for the next stage.
These are the same key decisions your existing Slide 3 is asking the mentor to confirm, but with the technical reasoning made explicit.
Proposed Methodology to Freeze